## Slide 1
EPRI IWC Meeting
SAE Medium and Heavy Duty Vehicle
Conductive Charging Task Force
Rodney McGee
Chairman
University of Delaware
Nov 18,19 2015
Atlanta Georgia

## Slide 2: Current Documents Under Development
EV Power Transfer using Three-phase Capable Coupler (J3068)
  Three-phase AC on-board or integrated chargers
EV Power Transfer using Overhead Coupler (J3105)
  Overhead DC charging
    Wireless charging
      Covered by sub-group under J2954

## Slide 3: Scope of J3068
  SAE has authorized a document for three-phase AC power transfer for electric vehicles
  Scope
    This document covers the general physical, electrical, functional, testing, and performance requirements for conductive power transfer to an electric vehicle using a coupler capable of, but not limited to, transferring three-phase AC power. It defines a conductive power transfer method including the digital communication system. It also covers the functional and dimensional requirements for the vehicle inlet, supply equipment outlet, and mating housings and contacts.
  Targeted towards charging at commercial and industrial locations or other places where three-phase power is available and preferred.

## Slide 4: J3068
  Document sponsor Jim McLaughlin from Volvo/Mack Trucks
  Early 40-page draft posted in work area on October 28
EVSE
  Evaluated to UL-2594, UL-2231
Cordset / Coupler
  Based on IEC Type-2
  Evaluated to UL-2251
Power levels and voltage
  Voltages USA 480VAC / Canada 600VAC
  Power example 160A 480VAC 3ø = 133kW
  Uses a digital communication over the Control Pilot which is harmonized with IEC 51851-1 Edition 3 Annex-D drafts

## Slide 5: Scope of J3105
  SAE has authorized a document for overhead power transfer
  Scope
    This document covers the general physical, electrical, functional, testing, and performance requirements for a mechanized (hands free) conductive power transfer system primarily for transit buses using an overhead coupler capable of, but not limited to, transferring DC power. It defines a conductive power transfer method including the curbside electrical contact interface, the vehicle connection interface, the electrical characteristics of the DC supply and the communication system. It also covers the functional and dimensional requirements for the vehicle connection interface and supply equipment interface
  Targeted towards in-route overhead charging, for example to recharge at transit bus during a short stop

## Slide 6: J3105
  Kick-off SAE meeting held on October 28, 2015
  Mark Kosowski, EPRI elected SAE document sponsor
  EPRI had a meeting in conjunction with an APTA meeting the following day on Wednesday November 11, 2015
  Both meetings were well attended with the majority of the electric transit companies attending

## Slide 7: Joining the Task Force (TEVHYB13)
Two documents are being developed under the SAE Medium and Heavy Duty Vehicle Conductive Charging Task Force
  EV Power Transfer using Overhead Coupler (J3105)
  EV Power Transfer using Three-phase Capable Coupler (J3068)
Download the form to join the task force
  http://bit.ly/sae-join
  Return to SAE Staff: elizabeth.perry@sae.org